Tender specification high-speed door NOVOSPRINT® Mono

Fabrication, supply and installation of a single side horizontal opening high speed door, with lateral winding up of the fabric door leaf as specified below. Vertical opening doors with winding mechanism above the door passage are not considered as equivalent. An optional physical ground closure must be possible..

Product quality and features of the door have to be type tested and certified in accordance with standard EN 13241-1. A warranty of max. 500 000 openings or max. 2 years for the first set of springs in the winding mechanism must be provided by the supplier.

Door frame: vertical jamb housing made of Sendzimir galvanised sheet steel profiles. Superior horizontal top cover made of steel, powder coated in RAL 9005 (jet black). The winding mechanism is integrated in the lateral jamb. Option: closed jamb housing for hand protection. The drive mechanism in the superior horizontal beam is made of massive, galvanised or paint coated steel components. The track rollers are based on ball bearings, the power transmission is made by a drive belt. Option: powder coating for vertical jamb, steel profile and horizontal beam in RAL colour: _____

Door leaf: single (option: double) skin fabric made of flexible polyester tissue, with double-sided PVC coating. Tear resistance min. 2.800 N / 50mm. Standard colour yellow. Integrated transparent PVC vision element from 1480 to 2000 mm above floor level. Options: other fabric colours; PVC-free fabric; fabric in accordance with food regulations (comparable FDA); fabric with antistatic finish. On demand: fabric with low flammability (DIN 4102 – B1).

Option: A physical ground closure of the door leaves in closed position by means of a flexible sealing lip has to be assured. Building tolerances with an unevenness of the floor of up to 10 mm have to be compensated.

Electric drive: motor integrated in the door frame with frequency control and holding brake.

Opening speed up to 1.75 m/s,

Option for single skin fabric: Opening speed up to 2.5 m/s.

Closing speed: max. 0.75 m/s (opto-electronic sensitive edge); option: max. 1.25 m/s (integrated light curtain).

Automatic closing delay adjustable to the second.

Emergency operation: manual, spring supported door opening, activation by lever fixed in the height of the control unit. Option: Automatic opening of the door if main switch is on “OFF” resp. in case of power breakdown.

Supply voltage: 1/N/PE 230V, protected with circuit breaker 1x C16 A.

Control: Frequency converter control system, protection class IP 54 (option: IP 65), fixed on the drive side. Front panel with switch Open-Stop-Close for operation and all-pole separating main switch. Opening by switch or signal device, the delay for automatic closing can be adapted by a timer. Connections for additional accessories are available. The function of output-relays is adjustable, e.g. for potential free indication door open / closed, for the connection of additional devices such as signal indicators or other accessories. Indication of operating status or malfunction by numerical code.

Option: variable opening width (Stop-X) can be activated by a selector switch.

Accessories for control and safety:

Options:

Key switch

Mushroom switch

Pull switch

Radio control receiver

Infrared light sensor

Radar motion sensor

Protection sensor Laser

Protection sensor Infrared

Induction loop detector

Infrared light barrier

Photo eye with reflector (passage surveillance)

Light curtain (passage surveillance)

Traffic lights

Flash lights

Other: ________________

Safety edge control: Supervision of the closing movement via an opto-electronic sensor integrated in the vertical rubber seal of the door leaf. Automatic reversing if triggered, in accordance with the latest regulations for power-operated windows, doors and gates. Option: light curtain integrated in the door leaf (contactless safety edge control, comparable to type C and D acc. to EN 12453)

Door sealing: between building and door frame with foam strip

Fixture: self - supporting frame construction, fixture behind or in the reveal and on the floor with solid, galvanised mounting brackets. The load transfer into the building has to be verified by the principal.

Operation Manual according to standard EN 82079-1.

Delivery to site and professional installation must be supplied. The electrical mains connection must be provided by the principal.

Quantity: _________________________

Clear Opening Width (mm):  __________

Clear Opening Height (mm): __________

(Notice: clear opening width min. 0.9 m, max. 2.5 m, clear opening height min. 1.7 m, max. 3.5 m. Depending on application and equipment the dimensions may change, if required please send a request)

Manufacturer notification:

Butzbach GmbH Industrietore

www.butzbach.com