Tender specification real glass stacking door SPACELITE® HTvision

Fabrication, supply and installation of a stacking door as specified below, with real glass panels and a vertical stacking of the open door panels in a cassette behind the lintel. The door must be equipped with toughened glass and observe the regulations for overhead sloped glazing, e.g. British Standard BS 6262 and BS 5516 or the GGF guide 7.1. Doors with torsion or tension springs for weight compensation, protruding hinges or dangling cables are not considered as equivalent in this tender.

Product quality and features of the door have to be tested and certified in accordance with standard EN 13241-1. The door meets following minimum requirements:

Air permeability (EN 12426): Class 3.

Resistance to wind load (EN12424): Class 2 to class 4 (depending on the door width)

Resistance to water penetration (EN 12425): Class 2

Door frame: solid aluminium tracks mill-finished (option: RAL colour coated or anodised according to DIN 17611). For shearing protection closed on three sides, with easily detachable track covers. Cables protected in a cable duct. Option: automatic operation, with integrated energy chain for power supply of safety edge.

Steel cassette: Galvanised, with drive unit on the right side, option: on the left side. Fixed at the lintel, without suspension from the ceiling.

Door panels with real glass infill: toughened double glazing, insulating glass with infill thickness 24 mm, Ug= 1.1 W/m2K. Up to 3.98 m door width without vertical inter-spacer, up to 5,5 m door width with one or two vertical inter-spacers. Panel height appr. 500 mm. Frame profiles in aluminium anodized in E6-C0 (EV1). Option: RAL colour coated or anodised in other colours. Interior glazing and finger protection profiles in PVC, colour RAL 7047 telegrey.

Electric drive: motor with electronic limit switch, electronic end position switch-off and thermal overheating protection, protection class IP 54 (Option: IP 65). Option: Mechanical overload protection, avoiding damages caused by obstruction of the door movement.

Emergency operation: mechanically via handle, option: via hoist chain.

Supply voltage: 3/N/PE 400V 50 Hz, protected with circuit breaker C10A.

Control: Control system, protection class IP 54 (option: IP 65). Option: Frequency converter for high opening speed. Front panel with switch Up-Stop-Down for operation and all-pole separating main switch. Standard: Opening in self-holding circuit/closing in dead-man‘s mode. Option automatic operation: door can be opened and closed in self-holding circuit. Connections for additional accessories are available. The function of output-relays is adjustable, e.g. for potential free indication door open / closed, for the connection of additional devices such as signal indicators or other accessories. Indication of operating status or malfunction by numerical code.

Option: variable opening height (Stop-X) can be activated by a selector switch.

Accessories for control and safety:

Options:

Key switch

Mushroom switch

Pull switch

Radio control receiver

Infrared light sensor

Radar motion sensor

Protection sensor laser

Protection sensor Infrared

Induction loop detector

Infrared light barrier

Photo eye with reflector (passage surveillance)

Light curtain (passage surveillance)

Traffic lights

Flash lights

Other: ________________

Safety: Anti-drop device with type examination test, integrated in the vertical guide tracks.

Option Safety edge control: In self-holding circuit via an opto-electronical sensor in accordance with the latest regulations for power-operated windows, doors and gates. Option: automatic closing with adjustable open time, with selection switch, in connection with a supervision of the closing area.

Door sealing: rubber seals between the individual door panels, between tracks and door panels with brush profiles, towards lintel and reveal with rubber seal lips, towards the floor with a double rubber-profile. Profiles made of EPDM.

Fixture: behind the reveal with solid, galvanised mounting brackets or within the reveal with galvanised steel plates.

Operation Manual according to standard EN 82079-1.

Delivery to site and professional installation must be supplied. The electrical mains connection must be provided by the principal.

Quantity: _________________________

Clear Opening Width (mm):  __________

Clear Opening Height (mm): __________

(Notice: max. door width without vertical inter-spacer 3.96 m. Max. door width with vertical inter-spacer 5.0 m

Manufacturer notification:

Butzbach GmbH Industrietore

www.butzbach.com